## Slide 1: High Rise Structures Assignment
Rudra Sai Teja
21CE31010

## Slide 2: Details of the building
Dimension: 50m x 30m
Location: Gandhinagar
No. of Storeys: G+50
Concrete: M30
Steel: Fe500

## Slide 3: Preliminary Design

## Slide 4
Floor | Size | Reinforcements
Ground floor – 10 | 1.8m x 1.8m | 70-36phi 10phi @ 300mm
11 – 30 | 1.5m x 1.5m | 69-36phi 10phi @ 300mm
35 – 50 | 1.2m x 1.2m | 24-36phi 10phi @ 300mm
Column details

## Slide 5
Beam details
(For all beams)
Dimensions: 600mm x 300mm
Top: 3-32 phi
Bottom: 3-32 phi
Stirrups: 8 phi @ 150mm c/c
Slab details
(For all slabs)
Thickness: 150mm
Longitudinal: 294 sq.mm/m
Transverse: 226 sq.mm/m
Drift = 0.00198

## Slide 6
Final Design

## Slide 7
Column | Floor | Size | Reinforcements
Periphery | Ground floor - 10 | 0.8m x 0.8m | 20-32phi 10phi @ 300mm c/c
 | 11 - 30 | 0.7m x 0.7m | 8-32phi 10phi @ 300mm c/c
 | 31 - 50 | 0.6m x 0.6m | 8-32phi 10phi @ 300mm c/c
Internal | Ground floor – 10 | 1.5m x 1.5m | 84-32phi 10phi @ 300mm c/c
 | 11 – 30 | 1.2m x 1.2m | 28-32phi 10phi @ 300mm c/c
 | 31 – 50 | 1m x 1m | 16-32phi 10phi @ 300mm c/c

## Slide 8: Beam details
(For all beams)
Dimensions: 600mm x 300mm
Top: 3-32 phi
Bottom: 3-32 phi
Stirrups: 10 phi @ 200mm c/c
Slab details
(For all slabs)
Depth: 250 mm
Longitudinal reinforcements: 300 sq. mm/m
Transverse reinforcements : 300 sq. mm/m

## Slide 9: Shear wall details
(For all shear walls)
Longitudinal reinforcements: 400 sq. mm/m
Transverse reinforcements : 400 sq. mm/m
Drift = 0.00174

## Slide 10: Mistakes done in preliminary submission
Very large column sizes
No shear wall provided
Floor finish was not considered in Dead Load
The drift was within standard limits, but this does not assure the stability

## Slide 11: Lessons learnt and adopted in final submission
The column sizes have been reduced by introducing more columns and structural form
Shear walls have been provided to tackle lateral loads
Floor finish has been considered in the Dead Load
Drift reduced from 0.00198 to 0.00174

## Slide 12: Conclusion
The structural form and shear wall together helps in reducing the drift
This also increase the floor efficiency as the column size has been reduced
Adopting any of the structural forms rather than the conventional design of the building has got more advantages